Extracting a Spice netlist from a SPECCTRAQuest topology

From SPECCTRAQuest:

* Initiate the Signal Probe command (Analyze -> SI/EMI Sim ->

Probe)

* Select the net and run your simulation, be sure to turn on the

"Save circuit files" toggle.

* In a UNIX terminal or MS-DOS command prompt, cd to the

appropriate signoise/case#/sim directory (where the *.spc files

are located), and enter "spc2spc"

From SigXplorer:

* Open the topology file

* Run the simulation

* In a UNIX terminal or MS-DOS command prompt, cd to the

appropriate signoise/case#/sim directory (where the *.spc files

are located), and enter "spc2spc"

***********************************************************************

OPTIONS and Usage for SPC2SPC

***********************************************************************

usage: spc2spc [options] infile

Options specifying output file(s):

-mapOut=<file>     Filename for connectivity map output

-spectreOut=<file> Filename for spectre language output

-spiceOut=<file>   Filename for spice language output

Options modifying processing:

-commentInfo       Include comments from source file before each

statement

-dir=<directory>   Write spice output file(s) to <directory>

-fileInfo          Include commented info about source file name and

line number

-flatten           Flatten the circuit so that no subckts remain

-h                 Print this help message

-includes          Add 'include' statements where needed.

-nelement          Retain transmission line 'N' elements

-rename=<node,elem,subckt>  Rename nodes, elems & subckts

Format codes are:

-alphanum    change to 8-char alpha followed by

numbers

-asis       do not change the name

-clean      change non-alphanumerics to '_'

-numeric    change to numbers

-sourceInfo Include commented source file text

-version    Print software version information

-welement   Use W element for all transmission

line models

-wminlen=<len>   Set minimum length for W

elements e.g. 10.0mil

(if no units specified: assumes meters)

Options for tuning ladder network generation

-s               Convert all single-line transmission lines to T models

-t=<RF_time>     Minimum rise/fall time in ps

-x=<seg_delay>   RLC segment delay in ps

Default operation:

If "rename" option not specified node names will be converted to

numbers

If neither "welement" or "nelement" is specified

-spectreOut=<file> Filename for spectre language output

-spiceOut=<file>   Filename for spice language output

Options modifying processing:

-commentInfo     Include comments from source file before each

statement

-dir=<directory> Write spice output file(s) to <directory>

-fileInfo        Include commented info about source file name and

line number

-flatten         Flatten the circuit so that no subckts remain

-h               Print this help message

-includes        Add 'include' statements where needed.

-nelement        Retain transmission line 'N' elements

-rename=<node,elem,subckt>  Rename nodes, elems & subckts

Format codes are:

alphanum    change to 8-char alpha followed by

numbers

asis        do not change the name

clean       change non-alphanumerics to '_'

numeric     change to numbers

-sourceInfo      Include commented source file text

-version         Print software version information

-welement        Use W element for all transmission line models

-wminlen=<len>   Set minimum length for W elements e.g. 10.0mil

(if no units specified: assumes meters)

Options for tuning ladder network generation

-s               Convert all single-line transmission lines to T

models

-t=<RF_time>     Minimum rise/fall time in ps

-x=<seg_delay>   RLC segment delay in ps

Default operation:

If "rename" option not specified

node names will be converted to numbers

If neither "welement" or "nelement" is specified

transmission line'N' elements will be replaced by ladder networks

If no output file is specified

Spice language output will be written to "main_gen.spc"