################################################## 
                                       # Technology part of the CPF # 
                              ################################################## 
set_hierarchy_separator /
set_power_unit uW 

# Specify libraries #
# define_library_set -name lib1d1v -libraries { /tools/techlibs/NangateOpenCellLibrary_PDKv1_3_v2010_12/Low_Power/Front_End/Liberty/LowPowerOpenCellLibrary_functional.lib }
  
define_library_set -name lib_bc -libraries {/tools/techlibs/NangateOpenCellLibrary_PDKv1_3_v2010_12/Front_End/Liberty/ECSM/NangateOpenCellLibrary_fast_ecsm.lib /tools/techlibs/NangateOpenCellLibrary_PDKv1_3_v2010_12/Low_Power/Front_End/Liberty/ECSM/LowPowerOpenCellLibrary_fast_ecsm.lib}
#define_library_set -name lib_typ -libraries {/home/yasir/NangateOpenCellLibrary_PDKv1_3_v2010_12/Front_End/Liberty/ECSM/NangateOpenCellLibrary_typical_ecsm.lib /home/yasir/NangateOpenCellLibrary_PDKv1_3_v2010_12/Low_Power/Front_End/Liberty/ECSM/LowPowerOpenCellLibrary_typical_ecsm.lib}
define_library_set -name lib_wc -libraries {/tools/techlibs/NangateOpenCellLibrary_PDKv1_3_v2010_12/Front_End/Liberty/ECSM/NangateOpenCellLibrary_slow_ecsm.lib /tools/techlibs/NangateOpenCellLibrary_PDKv1_3_v2010_12/Low_Power/Front_End/Liberty/ECSM/LowPowerOpenCellLibrary_slow_ecsm.lib}



# Specify special cells # 
## Isolation Cells ## 
define_isolation_cell -cells {"ISO_FENCE0N_X*"} -enable EN -valid_location to 
#define_isolation_cell -cells {"ISO_FENCE1_X*"} -enable EN -valid_location to 

## Power Switch Cells ## 
#define_power_switch_cell -cells HEADER_X* -stage_1_enable SLEEP -type header 
define_power_switch_cell -cells  HEADER_X* -power VVDD -power_switchable VDD -type header -stage_1_enable SLEEP


## Retention Cells ## 
  ## Retention Cells ## 
 define_state_retention_cell -cells  {"DFFR_X*"}   -restore_function RN
                       
                           # Always ON Cells ## 
 define_always_on_cell -cells {" AON_BUF_X*  AON_INV_X* "} 




                          ################################################## 
                                          # Design part of the CPF # 
                          ################################################## 
set_design topmodule 
# set_design xbus_hw_idct_rtl

# Declare power/ground nets # 
create_power_nets -nets VVDD -voltage 1.0 
create_power_nets -nets VDD 
create_ground_nets -nets VSS -voltage 0 
create_power_nets -nets SWVDD 

# Specify power domains # 
create_power_domain -name PD_default -default 
create_power_domain -name PD_xbus_hw_idct_rtl  -instances {XLXI_3} -shutoff_condition {!XLXI_2/pse} 
                                     
# Nominal operating conditions # 
create_nominal_condition -name off -voltage 0 
create_nominal_condition -name on -voltage 1.0 

#  Modes of operation # 
create_power_mode -name PM1 -domain_conditions {PD_default@on  PD_xbus_hw_idct_rtl@on} -default 
create_power_mode -name PM2 -domain_conditions {PD_default@on  PD_xbus_hw_idct_rtl@off} 


# Design rules # 
## Isolation rule ## 
  create_isolation_rule -name iso1 -from PD_xbus_hw_idct_rtl  -isolation_condition {XLXI_2/iso_en} -isolation_output low 


  # create_isolation_rule -name iso1 -from PD_xbus_hw_idct_rtl  -isolation_condition {powercontrol.iso_en} 
   #create_isolation_rule -name iso2 -to PD_default  -isolation_condition {powercontrol.iso_en} -isolation_output high 



                                   
## Power switch rule ## 
create_power_switch_rule -name psr1 -domain PD_xbus_hw_idct_rtl -external_power_net VVDD 

## State retention rule ## 
create_state_retention_rule -name st1 -domain PD_xbus_hw_idct_rtl -restore_edge {!XLXI_2/ret_en}  

#create_state_retention_rule -name st1 -domain PD_xbus_hw_idct_rtl -restore_edge {!powerontrol/ret_en}  




                                   ################################################## 
                                                   # Update libraries # 
                                   ################################################## 

# Associate library sets with nominal conditions # 
update_nominal_condition -name on -library_set lib_wc


# Update isolation the rules # 
update_isolation_rules -names iso1 -location to -cells {"ISO_FENCE0N_X*"} 

# Update powerswitch rules # 
update_power_switch_rule -name psr1 -prefix CPF_PS_ -cells " HEADER_X*"

# Specify timing constraints # 
update_power_mode -name PM1 -sdc_files idct.sdc 
update_power_mode -name PM1 -activity_file idct_rtlnew.tcf -activity_file_weight 100

# Describing power nets # 
create_global_connection -domain PD_default -net VVDD -pins "VDD vddo" 
create_global_connection -domain PD_default -net VSS -pins "VSS gndo" 
create_global_connection -domain PD_default -net VSS -pins "gndi swgnd" 
create_global_connection -domain PD_default -net SWVDD -pins swvdd 
create_global_connection -domain PD_xbus_hw_idct_rtl  -net VDD -pins VDD 
create_global_connection -domain PD_xbus_hw_idct_rtl -net VSS -pins VSS 

# update Power Domain # 
update_power_domain -name PD_default -internal_power_net VVDD 
update_power_domain -name PD_xbus_hw_idct_rtl -internal_power_net VDD 
end_design 

# END #