// Generated for: spectre
// Generated on: Oct  3 19:21:49 2017
// Design library name: wrk_Test2
// Design cell name: TESTBENCH_2
// Design view name: schematic
simulator lang=spectre
global 0 vdd!
parameters VGS=1.5 Vsin=0.5
include "$IHP_TECH/tech/spectre/mismatch.scs"
include "$IHP_TECH/tech/spectre/cornerDIO.scs" section=11
include "$IHP_TECH/tech/SGB25_MOS/library/spectre/cornerMOS_psp.scs" section=tt
include "$IHP_TECH/tech/SGB25V_HBT/spectre/cornerBIP.scs" section=typ
include "$IHP_TECH/tech/spectre/cornerRES.scs" section=11
include "$IHP_TECH/tech/spectre/cornerCAP.scs" section=11
include "$IHP_TECH/tech/spectre/cornerRCX.scs" section=11
include "$IHP_TECH/tech/spectre/statistics.scs"
include "$IHP_TECH/tech/spectre/models.all"

// Library name: wrk_Test2
// Cell name: TESTBENCH_2
// View name: schematic
V0 (net13 0) vsource dc=VGS type=dc
V8 (vdd! 0) vsource dc=3.5 type=dc
V13 (net10 net11) vsource type=sine delay=0 sinedc=0 ampl=0 freq=0
V12 (net11 0) vsource type=sine delay=0 sinedc=0 ampl=Vsin sinephase=0 \
        freq=1G
PORT1 (net12 0) port r=50 type=sine isnoisy=no noisetype=noisevoltage \
        noiseinterp=linear
PORT2 (net013 0) port r=50 num=2 type=dc isnoisy=no
R4 (net5 net12) resistor r=1K
R3 (net013 net9) resistor r=1
R2 (net010 0) resistor r=1.000m
R1 (net9 net5) resistor r=100K
R0 (net5 0) resistor r=100K
R8 (0 net10) resistor r=100
L1 (net13 net5) inductor l=1
E0 (net9 0 net5 net010) vcvs gain=1.0 type=vcvs
simulatorOptions options reltol=1e-3 vabstol=1e-6 iabstol=1e-12 temp=27 \
    tnom=27 scalem=1.0 scale=1.0 gmin=1e-12 rforce=1 maxnotes=5 maxwarns=5 \
    digits=5 cols=80 pivrel=1e-3 sensfile="../psf/sens.output" \
    checklimitdest=psf 
dcOp dc write="spectre.dc" save=allpub maxiters=150 maxsteps=10000 \
    annotate=status
dcOpInfo info what=oppoint where=rawfile
dc dc param=VGS start=0 stop=3.5 save=allpub oppoint=rawfile maxiters=150 \
    maxsteps=10000 annotate=status
sp sp ports=[PORT1 PORT2] start=10M stop=10G lin=500 annotate=status 
modelParameter info what=models where=rawfile
element info what=inst where=rawfile
outputParameter info what=output where=rawfile
designParamVals info what=parameters where=rawfile
primitives info what=primitives where=rawfile
subckts info what=subckts  where=rawfile
saveOptions options save=allpub currents=all subcktprobelvl=5 \
    saveahdlvars=all