Totally 11 modules in this microprocessor. Pc.v , ir.v, mem16k.v, ir.v, rc.v, clk.v, ir.v , register.v, accumulator.v, addsub.v..

But I think the problem is only with the mem16k.v

/*

* 50 Hz ( 1000ms / 20ms = 50 times in 1 sec ) clock Source for SAP1 computer

* each T state lasts for 40ms (2*20ms)

*/

module clk(c);

output c;

reg c;

initial begin

c = 1;	// clock begins at low state

end

always begin

#20;

c = ~c;

end

endmodule

module rc(clk, nCLR, T);

input clk;

input nCLR;

output[6:1] T;

reg[6:1] T;

initial begin

T[6:1] = 6'b000000;

end

always @(negedge clk)

begin

if( nCLR == 0)

T = 6'b000001;

else

begin

case(T)

6'b000000: T = 6'b000001;

6'b000001: T = 6'b000010;

6'b000010: T = 6'b000100;

6'b000100: T = 6'b001000;

6'b001000: T = 6'b010000;

6'b010000: T = 6'b100000;

6'b100000: T = 6'b000001;		// restart counting T states

endcase

end

end

endmodule

module pc( Cp, nCLK, nCLR, Ep, WBUSlower);

input Cp;

input nCLK;

input nCLR;

input Ep;

output[3:0] WBUSlower;

reg[3:0] nextPC;

initial begin

nextPC = 4'b0000;			// PC starts from zero

end

always @(negedge nCLK)			// negative edge of nCLK means positive edge of CLK

begin

if( Cp == 1)

/* Increment PC on every negative edge of nCLK

* (ie: positive edge of CLK - mid point of single T state

*/

begin

nextPC = nextPC + 1;

end

if ( nCLR == 0)

/* Reset Program Counter */

begin

nextPC = 4'b0000;

end

end

/*

* Keep WBUS in high impedence state when Ep is low (during this time some other module is using the WBUS)

* When Ep is high, output the contents of PC to WBUS

*/

assign WBUSlower = (Ep) ? nextPC : 4'bzzzz;

endmodule

module mem16K(data, address, CS, WE, OE);

parameter wordSize = 8;

parameter addressSize = 4;

inout [wordSize-1:0] data;

input [addressSize-1:0] address;

input CS, WE, OE;

reg [wordSize-1:0] dataReg;

reg [wordSize-1:0] memory [0:1<<addressSize];

// attach a tristate buffer to the databus

// if OE is active(low), connect datawires to the dataRegisters

// if OE is inactive(high), set datawires to high impedance for input

assign data = (!OE && WE && !CS)?dataReg:8'hzz;

// the reason cs is not put in the condition is

// internal wires are in accordance with databus

// but the data is not stored in memory so no problem

initial

begin

/* execution of a small program */

memory[0] = 8'h09;	// LDA 9H

memory[1] = 8'h1A;	// ADD AH

memory[2] = 8'h1B;	// ADD BH

memory[3] = 8'h2C;	// SUB CH

memory[4] = 8'hE0;	// OUT

memory[5] = 8'hF0;	// HLT

// dataReg = 8'h00;

// Instructions must be stored here before running SAP1

// memory[0] = 8'b00001011;		// LDA 08H ( ie: load contents from memory loc. 8 (B8) to acc)

// memory[1] = 8'b11100000;

// memory[2] = 8'b00011000;

// memory[3] = 8'b11100000;

//memory[2] = 8'b00001010;

//memory[3] = 8'b00001011;

//memory[2] = 8'b00011001; // ADD 09H

//memory[2] = 8'b00011011;

// data contents of memory

memory[9] = 8'h01;

memory[10] = 8'h02;

memory[11] = 8'h03;

memory[12] = 8'h04;

end

always @(WE or OE or CS)

begin

// incase of active(low) CS and active(low) WE

if (!CS && !WE)

begin

#1;

memory[address] = data;

//      $display(data);

end

end

always @(WE or OE or CS)

begin

if (!OE && !CS && WE)

dataReg = memory[address];

end

endmodule

module inputMAR( nLm, clk, WBUSlower, RAMaddress, RAM_nOE );

input nLm,clk;

input[3:0] WBUSlower;

output[3:0] RAMaddress;

reg[3:0] RAMaddress;

output RAM_nOE;

wire RAM_nOE;

reg tempReg;

initial begin

RAMaddress = 4'hz;

tempReg = 1;

end

always @(posedge clk)

begin

if ( nLm == 0)

begin

RAMaddress[3:0] = WBUSlower[3:0];

tempReg = 0;

end

end

assign RAM_nOE = (tempReg) ? 1:0;

endmodule

module ir( nLi, clk, clr, nEi, WBUS, WBUSlower, OPCODE, ADDRESS );

input nLi;

input clk;

input clr;

input nEi;

input[7:0] WBUS;

output[3:0] WBUSlower;

output[3:0] OPCODE;

output[3:0] ADDRESS;

reg[7:0] IR;			// internal copy of the contents of IR

reg[3:0] OPCD;

reg[3:0] ADDR;

initial begin

IR = 8'hzz;

OPCD = 4'bzzzz;

ADDR = 4'bzzzz;

end

always @(posedge clk)

begin

if( nLi == 0 )

begin

IR = WBUS;

OPCD = IR[7:4];

ADDR = IR[3:0];

end

if( clr == 1 )

begin

IR = 8'hzz;

OPCD = 4'bzzzz;

ADDR = 4'bzzzz;

end

end

assign WBUSlower = (nEi) ? 4'bzzzz : ADDR;

assign OPCODE = (1)? OPCD : 4'bzzzz;

assign ADDRESS = (1)? ADDR : 4'bzzzz;

endmodule

module accumulator(out, outStd, in, EA, LA, CLK);

parameter wordSize = 8;

output [wordSize-1:0] out, outStd;

input [wordSize-1:0] in;

input EA, LA, CLK;

reg [wordSize-1:0] outStd;

wire [wordSize-1:0] out;

// tristate output => out

assign out = (EA)?outStd:8'hzz;

always @(negedge CLK)

begin

if (!LA)

outStd = in;

end

endmodule

module register(out, in, LB, CLK);

parameter wordSize = 8;

output [wordSize-1:0] out;

input [wordSize-1:0] in;

input LB, CLK;

reg [wordSize-1:0] out;

initial

out = 8'b00;

always @(negedge CLK)

begin

if (!LB)

// store input => out

out = in;

end

endmodule

module addersubtractor(out, inputA, inputB, SU, EU);

parameter wordSize = 8;

parameter addressSize = 4;

output [wordSize-1:0] out;

input [wordSize-1:0] inputA;

input [wordSize-1:0] inputB;

input SU;

input EU;

wire [wordSize-1:0] out;

assign out = (EU)?( (SU)?(inputA - inputB):(inputA + inputB)):8'bzz;

endmodule

module register(out, in, LB, CLK);

parameter wordSize = 8;

output [wordSize-1:0] out;

input [wordSize-1:0] in;

input LB, CLK;

reg [wordSize-1:0] out;

initial

out = 8'b00;

always @(negedge CLK)

begin

if (!LB)

// store input => out

out = in;

end

endmodule

module binarydisplay(in,out);

input[7:0] in;

output reg[7:0] out;

always @(in)

begin

out[0]=in[0];

out[1]=in[1];

out[2]=in[2];

out[3]=in[3];

out[4]=in[4];

out[5]=in[5];

out[6]=in[6];

out[7]=in[7];

end

endmodule